## Slide 1: Number Systems
Last Week
Analog and Digital Signals
Number Systems
Arithmetic Operations in Binary System
One’s Complement and Two's Complement
Signed Numbers
This Week
Floating Point Numbers
Arithmetic Operations with Signed Numbers
Addition and Subtraction
Multiplication and Division

## Slide 2: Floating Point Numbers
We can represent very small numbers (e.g. 0.00000000000000000001) and very large numbers (e.g. 999999999999999999999) using floating-point numbers in scientific format.
For example, in IEEE-754 standard, floating-point numbers are represented in 32-bits. 1 bit for the sign, 8 bits for exponent, and 23 bits for significand.
There are 64-bit and 80-bit representations as well.
Sign Exponent Significand
1-bit
8-bits
23-bits
32-bit representation
(biased)

## Slide 3: Normalization
A binary number can be in different forms in scientific notation.
1 = 0.1x21 = 0.01x22 = …
As a standard, we make sure that the whole part of the number is 1. This process is called normalization.
For example, we normalize the number 100110010112 by converting it to 1.0011001011×210.

## Slide 4: Biased Exponent
In floating point representation, we do not store the exponent directly. Instead, we use the biased exponent. Exponent bias is calculated by this formula:
Bias = 2[exponent bit count]-1-1
In 32-bit floating point representation, the exponent bias is 127 (28-1 -1). So, we add 127 to the exponent.
The original exponent may vary between -126 and 128. But we need to store a positive number. That’s why we add bias to the original exponent. Biased exponent is always a positive number.
In floating point representation, when all the bits are 0, then the number is considered to be 0. When exponent part is all 1’s and significand part is all 0’s, then the number is considered to be infinite.

## Slide 5: Floating Point Numbers
Example: Let’s convert 1.0011001011×210 to floating number.
Since the number is positive, the sign bit is 0. The exponent is 10. So, biased exponent is 10+127 (bias)=137=100010012. And finally, the significand is 00110010112.
If the number above were negative, the result would remain the same, but the sign bit would be set to 1.
Floating point representation lets us store larger numbers using less bits. For instance, let’s take the largest number that can be stored 32-bit floating point representation. If we wanted to store the same number in binary form, we would need 129 bits.
0 10001001 00110010110...0
1-bit
8-bits
23-bits

## Slide 6: Floating Point Numbers
In a 4-bit floating point representation, let’s assume that the sign part is 1 bit, biased exponent part is 2 bits, and the significand is 1 bit.
Let’s analyze the numbers that can be stored using this representation.
Bias = 22-1-1 = 1
All the positive numbers that can be stored are;
1.0×2-1 = 0.5 1.1×2-1 = 0.75
1.0×20 = 1 1.1×20 =1.5
1.0×21 = 2 1.1×21 = 3
1.0×22 = 4 1.1×22 = 6
Sign Biased Exponent Significand
1 bit
2 bits
1 bit

## Slide 7: Floating Point Numbers
Although not shown in the chart above, we also have the same numbers with negative signs on the number axis. With 4 bits, we can store 2⁴ = 16 distinct numbers. As demonstrated, the gaps between numbers increase as the values grow larger.
As you can see, we can store 3 different numbers in the range between 0.5 and 1, and the same applies to the ranges between 1 and 2, as well as 2 and 4.
If the exponent were 1 bit and the significand 2 bits, we'd still have 4 bits in total, allowing for 16 different bit combinations. However, the represented numbers would change to 1, 1.25, 1.5, 1.75, 2, 2.5, 3, and 3.5.
In this scenario, the gaps between the numbers would be smaller, allowing for finer precision, but the range of representable numbers would be limited to relatively smaller values.
0.5
0.75
1
1.5
3
4
6
2

## Slide 8: Arithmetic Operations on Signed Numbers
In this section, we will use two’s complement form.
Addition and subtraction:
The sum of two positive numbers is a positive number.
Example: 00001001 (9)
+ 00000100 (4)
00001101 (13)
The sum of a positive number and a smaller negative number is a positive number. We ignore the carry bit.
Example: 00001001 (9)
+ 11111010 (-6)
100000011 (3)

## Slide 9: Arithmetic Operations on Signed Numbers
The sum of a positive number and a greater negative number is a negative number in two’s complement form.
Example: 00001000 (8)
+ 11110100 (-12)
11111100 (-4 in two’s complement form)
The sum of two negative numbers is a negative number. We ignore the carry bit.
Example: 11111101 (-3)
+ 11111110 (-2)
111111011 (-5)

## Slide 10: Arithmetic Operations on Signed Numbers
When adding signed numbers, any carry bit is ignored. However, there are two exceptional cases: when both numbers are positive, but the sign bit is 1, and when both numbers are negative, but the sign bit is 0. In both cases, an overflow has occurred, indicating that an additional bit is needed to represent the sum.
Example: 01101110 (110)
+ 00011001 ( 25)
10000111 (overflow)
Subtraction of signed numbers is simply a variation of addition. We convert the number to be subtracted into its two's complement form and then add the two numbers.
Example: 8-3 operation is performed as 8+(-3).
00001000 (8)
+ 11111101 (-3)
100000101 (5)

## Slide 11: Multiplication
Multiplication can be performed by adding the number to itself as many times as necessary. For example, 4×2 is considered as 4+4. When the multiplier value is large, it becomes tedious, so the partial product method is used.
First, it is checked whether the multiplicand and the multiplier have the same sign, and the sign of the result is determined.
Then, we convert negative numbers to positive.
Then, starting from LSB of the first number, partial products are obtained. If the multiplier is 1, the multiplicand itself is used; if it is 0, a partial product of 0 is obtained. Each partial product is shifted left by one.
All partial products are summed to obtain the final product.
Then, from the first step, if the product must be negative, we convert the number to two’s complement form. If the product must be positive, we leave the result as it is. Then we add a sign bit to the left.

## Slide 12: Multiplication
Example: Let’s calculate 25×(-4)
11001
× 100 -4 converted to 4
00000 1st partial product
+ 00000 2nd partial product (shifted left by 1 bit)
000000 subtotal
+ 11001 3rd partial product (shifted left by 2 bits)
1100100 absolute value of the product
Since the product must be negative, we convert the result to two’s complement form.
Two’s complement of 11001002 is 00111002.
Eventually, we add a sign bit and get the final product: 100111002.

## Slide 13: Division
Division can be performed with subtraction. As we know, subtraction is performed by addition. So, division can also be performed by addition. The quotient can be calculated by subtracting the divisor from the dividend multiple times. The number of subtraction operations gives us the quotient. We do the division operation as follows:
- First, we check both numbers have the same sign and detect the sign of the result.
- Then, we convert negative numbers to positive.
- Then, we assign 0 to quotient.
- Then, we subtract the divisor from the dividend. We get the partial remainder and increase quotient by 1. If the partial remainder is negative, then the division is considered as complete. If the partial remainder is positive, we proceed to the next step.
- We subtract the divisor from the partial remainder and increase quotient by 1. If the result is positive, then we repeat the same operation with the next partial remainder. If the result is 0 or negative, then the operation is considered as complete.

## Slide 14: Division Example
Example: Let’s do the operation 25/6.
Since both numbers are positive, the result should be positive.
25 = 000110012 and 6 = 000001102
We assign 0 to quotient and subtract the divisor from the dividend.
00011001
+ 11111010 (Two’s complement form of 6)
100010011 (carry bit is ignored) Since partial remainder is positive; quotient=0+1=1
We subtract the divisor from the partial remainder.
00010011
+ 11111010
100001101 (carry bit is ignored) Since partial remainder is positive; quotient=1+1=2
We subtract the divisor from the partial remainder again.
00001101
+ 11111010
100000111 (carry bit is ignored) Since partial remainder is positive; quotient =2+1=3

## Slide 15: Division Example (Continuing)
We subtract the divisor from the partial remainder again.
00000111
+ 11111010
100000001 (carry bit is ignored) Since partial remainder is positive; quotient=3+1=4
We subtract the divisor from the partial remainder again.
00000001
+ 11111010
11111011 There’s no carry bit. The result is negative. The division is completed. The result of the division operation is quotient’s current value, which is 4 (000001002 in binary).
The remainder is the result of previous subtraction (attention, not the last one), which is 000000012