## Slide 1: Number Systems
Last Week
Floating Point Numbers
Arithmetic Operations on Signed Numbers
Addition and Subtraction
Multiplication and Division
This Week
Hexadecimal Number System
Octal Number System
Conversion Between Hexadecimal/Octal/Decimal Systems

## Slide 2: Hexadecimal Number System
There are 16 figures in hexadecimal system. First ten figures are numbers from 0 to 9, and the last 6 figures are the letters from A to F. It gets difficult to write and read large binary numbers. But computers work only with binary numbers. Considering that a computer command consists of 32 bits, it would require a massive effort to write a computer program using binary system. Using hexadecimal system instead makes this process easier. In hexadecimal system, each digit corresponds to a 4-bit binary number.
Decimal | Binary | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 3: Hexadecimal Number System
In hexadecimal system F16 is followed by 1016 and continues as 1116,1216,...,1916,1A16, ..., 1F16.
Two digits in hexadecimal can represent numbers between 0 (0016) and 255 (FF16).
To convert a binary number to hexadecimal, we divide the binary number into groups of four. We start grouping from the right side of the whole part, and from the left side of the fractional part. Remember that we can add 0’s to the left side of the whole part, and to the right side of the fractional part.

## Slide 4: Example
Let’s convert 0100011111100012 to hexadecimal. First, we need to divide this number into groups of four.
0010 0011 1111 0001 (Notice that, we add an extra 0 to the left)
2 3 F 1
Then, (010001111110001)2 = (23F1)16
Let’s convert 1011001101.1100102 to hexadecimal.
0010 1100 1101 . 1100 10002 = 2CD.C816.
Notice that we add extra 0’s to the left side of the whole part and to the right side of the fractional part.

## Slide 5: Conversion
To convert a hexadecimal number to binary, we convert each digit independently, and then concatenate the result.
Example: Let’s convert 4A3F16 to binary.
4 A 3 F
0100 1010 0011 1111
4A3F16 = 01001010001111112
Example: Let’s convert ABC.DE16 to binary.
ABC.DE16 = 101010111100.110111102

## Slide 6: Conversion
There are two ways to convert hexadecimal numbers to decimal.
1st Way
We convert the number to binary, then convert to decimal.
Example: 2A16 = 001010102= 25+23+21= 4210
2nd Way
We convert the number to binary using sum of weights method.
Example: Let’s convert (1B.1A)16 to decimal.
(1B.1A)16 = 1×161+11×160+1×16-1+10×16-2 =16+11+1/16+10/256 27.1

## Slide 7: Conversion
To convert from decimal to hexadecimal, we divide the number to 16 repeatedly and take the remainders.
Example: Let’s convert 257710 to hexadecimal.
2577 16
-16 161 16
97 -160 10 A16
- 96 1
17
- 16 Then, 257710 = A1116
1

## Slide 8: Example
Example: Let’s convert 123.256 to hexadecimal.
We need to convert the whole part and the fractional part separately.
123.536  7B.41816
Whole Part |  | 
 | Quotient | Remainder
123/16 | 7 | 11 (B)
7/16 | 0 | 7
Fractional Part | 
0.256×16 | 4.096
0.096×16 | 1.536
0.536×16 | 8.576

## Slide 9: Addition on Hexadecimal Numbers
In hexadecimal addition, we add up each digit’s decimal values. If the sum is less than or equal to 15, we write the corresponding hexadecimal digit to the result. If the sum is greater than 15, than we subtract 16 from the sum and write the difference to the sum and carry 1 to the next digit.
Example: 2916 916+A16 = 910+1010 = 1910
+ 1A16 19-16 = 3 carry 1
4316 2+1+1(carry) = 4
Example: EF16 F16+B16 = 1510+1110 = 2610
+ 9B16 26-16 = 10 = A16 carry 1
18A16
E16+916+1(carry) = 1410+910+1=2410
24-16 = 8 carry 1

## Slide 10: Subtraction on Hexadecimal Numbers
As you remember, we do binary subtraction by converting the second number to two’s complement and then adding up these two numbers.
We can use the same method to do hexadecimal subtraction. To do this, we first convert the second number to binary, calculate two’s complement, and convert back to hexadecimal. Then add the numbers.
Example: Let’s calculate 2516 - 1B16
1B16 = 000110112. Two’s complement of 00011011 is 111001012 which is E516.
2516
+ E516
10A16 The result is 0A (we ignore the carry bit)

## Slide 11: Octal Number System
Octal system is not as widely used as hexadecimal system. In octal system, numbers from 0 to 7 are used. 7 is followed by 10.
0,1,…,6,7,10,11,…,16,17,20,21,…
We convert octal numbers to decimal using sum of weights method.
Example: Let’s convert 12348 to decimal.
12348 = 1×83 + 2×82 + 3×81 + 4×80 = 66810
Example: Let’s convert 12.348 to decimal.
12.348 = 1×81 + 2×80 + 3×8-1 + 4×8-2 = 8+2+3/8+4/64  10.44

## Slide 12: Conversion
To convert a decimal number to octal, we divide the number by 8 repeatedly. Then, we concatenate the remainders and form the octal number.
Example: Let’s convert 12310 to octal.
123 8
- 8 15 8
43 - 8 1
- 40 7
3
Then, 12310 = 1738

## Slide 13: Conversion
Example: Let’s convert 34.4510 to octal.
34.45  42.3468
Conversion from octal to binary is just like hexadecimal system. We convert each digit to 3-bit binary numbers and concatenate these numbers.
Example: Let’s convert 4568 to binary.
4568 = 1001011102
Example: Let’s convert 56.348 to binary.
56.348 = 101110.0111002
Whole Part |  | 
 | Quotient | Remainder
34/8 | 4 | 2
4/8 | 0 | 4
Fractional Part | 
0.45×8 | 3.6
0.6×8 | 4.8
0.8×8 | 6.4

## Slide 14: Conversion
Conversion of binary numbers to octal is just like hexadecimal numbers. The only difference is that we divide the binary number into groups of four. We start grouping of the whole part from right to left, and the fractional part from left to right. Remember that we can add extra 0’s to the left of the whole part, and to the right of the fractional part.
Example: Let’s convert 1011100012 to octal.
1011100012 = 5618
Example: Let’s convert 10011.110102 to octal.
010 011 . 110 100 (Divided into groups of three and added extra 0’s.)
Then, 10011.110102 = 23.648

## Slide 15: Conversion
To convert from octal to hexadecimal, we first convert from octal to binary, then to hexadecimal. Likewise, to convert from hexadecimal to octal, we first convert from hexadecimal to binary, then to octal.
Example: Let’s convert 45.638 to hexadecimal.
45.638 = 100101.1100112
0010 0101 . 1100 1100 (Divide the binary number to groups of four)
Then, 45.638 = 25.CC16
Example: Let’s convert A2.B316 to octal.
A2.B316 =10100010.101100112
010 100 010 . 101 100 110 (Divide the binary number to groups of three)
Then, A2.B316 = 242.5468