## Slide 1: BOOLEAN ALGEBRA (Continuing)
Canonical Forms
- Sum of Products (SoP) Form
Standard Sum of Products Form
Minterms
- Product of Sums (PoS) Form
Standard Products of Sum Form
Maxterms
- Conversion Between Standard SoP and PoS Forms

## Slide 2: Canonical Forms
Logical expressions can be written in Sum of Products (SoP) form and Product of Sums (PoS) form. These forms help us standardize the logical expressions. They also help us understand, simplify, and implement the logical expressions easily and systematically.
Sum of Products Form: An expression which is in SoP form, consists of the sum of products of the variables. We get the product by multiplying the variables or complements of variables. A product does not necessarily have all the variables in it.
The expressions ABC+A’B+BC’D’ and A’+AB+BC’ are in SoP form. Because we multiply only variables in each term. However, if we multiply something complicated like (ABC)’ in a term, we cannot say that the expression is in SoP form.
We can convert any expression into SoP form using Boolean algebra.

## Slide 3: Canonical Forms
Example: Let’s convert A’B(C+BD’) into SoP form.
We apply the distributive law.
A’B(C+BD’) = A’BC + A’BD’
Standard Sum of Products Form: In SoP form, a term may not have all the variables in it. However, in standard SoP form, each term must have all the variables in it. To convert an expression in SoP form into Standard SoP form, we must extend all the terms with missing variables.
Example: Let’s convert F(A,B,C) = A.B’+A.C into standard SoP form.
We need to extend the first term with (C+C’) and the second term with (B+B’).
AB’+AC = AB’(C+C’)+A(B+B’)C = AB’C+AB’C’+ABC+AB’C = AB’C+AB’C’+ABC

## Slide 4: Canonical Forms
Example: Let’s convert F(A,B,C) = A+BC+A’C into standard SoP form in a more practical way. We create a table for conversion.
F(A,B,C) = AB’C’+AB’C+ABC’+ABC+A’BC+ABC+A’B’C+A’BC
= AB’C’+AB’C+ABC’+ABC+A’BC+A’B’C
We will use Standard SoP form to populate truth tables and Karnaugh maps.
A | BC | A’C
ABC | ABC | ABC
100 | 011 | 001
101 | 111 | 011
110 |  | 
111 |  | 

## Slide 5: Minterms
Each term in an expression in standard SoP form is called a minterm. An expression with n variables has 2n minterms. For example, an expression with 3 variables has 8 minterms. Each minterm in an expression corresponds to a single row (with output 1) in the truth table.
mindex denotes the minterm with that index. Index can easily be calculated by the values that make the minterm 1. For example, the term AB’C’ will be 1 if and only if A=1, B=0, and C=0 (ABC=100). (100)2 is 4 in decimal. So, AB’C’ is m4.
Variables |  |  | Minterms | 
A | B | C | Term | Symbol
0 | 0 | 0 | A'B'C' | m0
0 | 0 | 1 | A'B'C | m1
0 | 1 | 0 | A'BC' | m2
0 | 1 | 1 | A'BC | m3
1 | 0 | 0 | AB'C' | m4
1 | 0 | 1 | AB'C | m5
1 | 1 | 0 | ABC' | m6
1 | 1 | 1 | ABC | m7

## Slide 6: Minterms
Example: Let’s generate the truth table of F=A’B’C+A’BC+ABC.
Inputs |  |  | Output (F) | Minterms
A | B | C |  | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | A'B'C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | A'BC
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | ABC
In short, we use the  symbol to abbreviate the expressions in standard SoP form.
F(A,B,C) = m1 + m3 + m7 =  (1,3,7)

## Slide 7: Canonical Forms
Product of Sums (PoS) Form: An expression which is in PoS form, consists of the products of sums of the variables. .
The expressions (A+B’)(A’+B+C) and A(A’+B)(B+C’) are in PoS form. However, if we add something complicated like (ABC)’ in a term, we cannot say that the expression is in PoS form.
Standard Product of Sums Form: In PoS form, a term may not have all the variables in it. However, in standard PoS form, each term must have all the variables in it. To convert an expression in PoS form into Standard PoS form, we must extend all the terms with missing variables.
Example: Let’s convert F(A,B,C)=(A+B’)(B+C) into standard PoS form.
(A+B’)(B+C) = (A+B’+C.C’)(A.A’+B+C)
= (A+B’+C).(A+B’+C’).(A+B+C).( A’+B+C)

## Slide 8: Maxterms
Each term in an expression in standard PoS form is called a maxterm. An expression with n variables has 2n maxterms. For example, an expression with 3 variables has 8 maxterms. Each maxterm corresponds to a single row (with output 0) in the truth table.
Variables |  |  | Maxterms |  | Minterms | 
A | B | C | Term | Symbol | Term | Symbol
0 | 0 | 0 | A+B+C | M0 | A'B'C' | m0
0 | 0 | 1 | A+B+C' | M1 | A'B'C | m1
0 | 1 | 0 | A+B'+C | M2 | A'BC' | m2
0 | 1 | 1 | A+B'+C' | M3 | A'BC | m3
1 | 0 | 0 | A'+B+C | M4 | AB'C' | m4
1 | 0 | 1 | A'+B+C' | M5 | AB'C | m5
1 | 1 | 0 | A'+B'+C | M6 | ABC' | m6
1 | 1 | 1 | A'+B'+C' | M7 | ABC | m7
Mindex denotes the maxterm with that index. Index can easily be calculated by the values that make the maxterm 0. For example, the term A’+B+C will be 0 if and only if A=1, B=0, and C=0 (ABC=100). (100)2 is 4 in decimal. So, A’+B+C is M4.
Maxterms and minterms are complements of each other.
M0 = m0’ and m0 = M0’

## Slide 9: Maxterms
Example: Let’s generate the truth table of F(A,B,C)=(A+B+C).(A+B’+C).(A’+B+C).(A’+B+C’).(A’+B’+C)
Inputs |  |  | Output (F) | Maxterms
A | B | C |  | 
0 | 0 | 0 | 0 | A+B+C
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | A+B'+C
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | A'+B+C
1 | 0 | 1 | 0 | A'+B+C'
1 | 1 | 0 | 0 | A'+B'+C
1 | 1 | 1 | 1 | 
In short, we use the  symbol to abbreviate the expressions in standard PoS form.
F=  (0,2,4,5,6) = M0∙M2∙M4∙M5∙M6

## Slide 10: Conversion Between Standard SoP and PoS Forms
Example: Let’s convert F(A,B,C) = (4,5,6,7) into maxterms.
Inputs |  |  | F | F’
A | B | C |  | 
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
We will do double negation and find out (F’)’.
The complement of function F is;
F’(A,B,C) =  (0,1,2,3) = m0+ m1+m2+m3
The complement of F’ is equal to F. So;
F(A,B,C) = (m0+ m1+m2+m3)’ = m0'. m1'.m2'.m3'
= M0. M1.M2.M3
=  (0,1,2,3)
Remember that, minterms and maxterms are complements of each other. M0 = m0’ and m0 = M0’

## Slide 11: Conversion Between Standard SoP and PoS Forms
Example: Let’s convert the following expression in standard SoP form to standard PoS form.
F(A,B,C) = AB’C+A’BC+AB’C’+ABC+A’B’C
1st way
All the combinations that make F=1 are 101, 011, 100, 111 and 011. It means that, all other combinations 000, 010, and 110 make F=0. Therefore, the maxterms are (A+B+C), (A+B’+C), and (A’+B’+C).
F(A,B,C)= (A+B+C).(A+B’+C).(A’+B’+C)
2nd Way
We can write the expression in the following form.
F(A,B,C) = (1,3,4,5,7)
Since maxterms are complements of minterms, we can say that;
F(A,B,C) =  (1,3,4,5,7) =  (0,2,6)

## Slide 12: Simplification
Example: Let’s find the simplest form of F given in the truth table below, using minterms and maxterms.
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
First, let’s write the F using minterms, and then simplify.
F(A,B,C) =  (0,2,3,5,7) = A'B'C' + A'BC’ + A'BC + AB'C + ABC
= A'C'(B'+B) + A’BC + AC(B’+B) = A’C’+A’BC+AC
= A’C’ + C(A’B+A) = A’C’+C(A+B) = A’C’+AC+BC
We could simplify the expression in another way.
F(A,B,C) =  (0,2,3,5,7) = A'B'C' + A'BC’ + A'BC + AB'C + ABC
= A'C'(B'+B) + A’BC + AC(B’+B) = A’C’+A’BC+AC
= A’(C’+BC)+AC = A’(B+C’)+AC = A’C’+AC+A’B
Both results are correct.

## Slide 13: Simplification
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
First, let’s write the F using maxterms, and then simplify.
F(A,B,C) =  (1,4,6) = (A+B+C').(A’+B+C).(A'+B'+C)
= (AA’+AB+AC+A’B+BB+BC+A’C’+BC’+C’C)( A'+B'+C)
= (AB+AC+A’B+B+BC+A’C’+BC’)( A'+B'+C)
=(B+AC+A’C’)(A’+B’+C)
= A’B+BB’+BC+A’AC+AB’C+ACC+A’A’C’+A’B’C’+A’C’C
= A’B+BC+AB’C+AC+A’C’+A’B’C’
= A’B+B’(AC+A’C’)+ AC+A’C’
= A’B+AC+A’C’
As you can see above, this simplified expression is the same as we have found by simplifying minterms. We can also find the other correct result by doing the simplification in another way.